## Slide 1
Tissue Optical Properties
Mohammed Alwan Kadhum

## Slide 2: Introduction
Interaction between Light and Tissue
  Reflection
Refraction
Absorption
Optical Signal
Light Source
Fluorescence
Scattering
Tissue
Depends on
  Constituents of tissue
  Optical properties of tissue
  Propagation of light

## Slide 3: Absorption
Extraction of energy from light by a molecular species
Diagnostic applications: Transitions between two energy levels of a molecule that are well defined at specific wavelengths could serve as spectral fingerprint of the molecule
  Various types of Chromophores (light absorbers) in Tissue
  Wavelength-dependent absorption
  Tumor detection and other physiological assessments (e.g. pulse- oximetry)
Therapeutic applications: Absorption of energy is the primary mechanism that allows light form a source (laser) to produce physical effects on tissue for treatment purpose
  Lasik (Laser Assisted in situ Keratomileusis) Eye Surgery, Tatoo Removal, PDT

## Slide 4: Absorption
‘ ’ ’
Absorption occurs when the photon frequency matches the frequency associated with the molecule s energy transition
  Electrons absorb the energy of the light and transform it into vibrational motion
  The absorption of a photon results in:
  quantized change in charge separation
  quantized excitation of vibrational modes
  Electrons interact with neighboring atoms  convert vibrational energy into thermal energy

## Slide 5: Absorption
Each electronic energy
levels is associated with many vibrational energy levels
Vibrational Energy Level
S1
Absorption of UV and visible light promotes transition between electronic energy levels
Electronic Energy Level
S0
Potential Energy
Absorption of infrared light promotes transitions between vibrational energy levels

## Slide 6: Absorption
Absorption Cross-section,
 [m2]
  Consider a chromophore idealized as a sphere with a particular geometrical size.
  Consider that this sphere
a
a
  Q  A
blocks incident light and casts a shadow, which constitutes absorption.
The size of absorption shadow
= absorption cross-section
Qa: absorption efficiency

## Slide 7
Absorption
Pin =IoA
Pabs = Ioa
Pout = Io(A-a)
Incident Beam
Outgoing Beam
Area =A
Area = a
-
=
Pout = Io(A-a) area = A - a
a
I
 Pabs

o

## Slide 8: Absorption
Assumptions
  Cross section is independent of relative orientation of the impinging light and absorber uniform distribution of Na (molecules/cm3) identical absorbing particles
Absorption Coefficient, ma [1/m]
Ma  Na  a
Absorption cross-sectional area per unit volume of medium
Absorption mean free path, la [m]
a
a

l  1
Represents the average distance a photon travels before being absorbed

## Slide 9: Absorption
Transmission and Absorbance (macroscopic view)
Transmission
T  I
Absorbance (attenuation, or optical density)
Io
A  log(T )  log  Io 
 I 
 

## Slide 10: Absorption
Lambert – Beer Law:
  The linear relationship between absorbance and concentration of an absorbing species.
  Relates μα, transmission, and absorbance
I  I e a b o
a  Na  a
= absorption cross-sectional area [cm2]
IO = The intensity entering the sample at z = 0 [w/cm2]
a
O
I

 Pabs
I = The intensity of light leaving the sample [w/cm2] b = pathlength traveled in the sample [cm]

## Slide 11: Absorption
Absorbers in Tissue
NIR
UV
VISIBLE
NIR
UV-VIS
Hemoglobin
Lipids
Water
*
DNA
Hemoglobin
Lipids
Structural protein
Electron carriers*
Amino acids*
* Absorbers that fluoresce when excited in the UV-VIS

## Slide 12: Absorption
UV Absorption
Protein, amino acid, fatty acid and DNA absorption dominate UV absorption
Protein
Amino Acid
Dominant ‘non-water’ constituent of all soft tissue, ~ 30%
Absorption properties
determined by peptide bonds and amino acid residues
Peptide excitation about λ =
190 nm
Amino acids absorption at λ = 210 - 220 nm and 260 – 280 nm
Peptide
DNA
  Absorbs radiation for λ ≤ 320 nm
Large water absorption λ< 180 nm

## Slide 13: Absorption
Infrared Absorption
Protein IR absorption peaks at 6.1, 6.45, and 8.3 μm due to amide excitation
Absorption depth ≤ 10 μm in λ
= 6-7 μm region
Water absorption peak at 0.96, 1.44, 1.95, 2.94 and
  μm
    Absorption depth
      ~ 500 mm at λ = 800 nm
      <1 μm at λ=2.94 μm
      ≤ 20 μm throughout λ ≥ 6 μm

## Slide 14: Absorption
106
Main Absorbers at visible and NIR
105
103
104
Hb
Hemoglobin
Lipid
Hemoglobin
102
Extinction Coeff (1/cm M)
HbO
2
400 500 600 700 800 900 1000
WAVELENGTH (NM)
Each hemoglobin has 4 heme (Fe2+) sites to bind O2
Responsible for oxygen transport
•HbO2 and Hb
oxygen saturation is an indicator of oxygen delivery and utilization as well as metabolic activity

## Slide 15: Absorption
106
105
Hemoglobin
Responsible for oxygen transport
  HbO2 and Hb
  oxygen saturation is an indicator of oxygen delivery and utilization as well
103
104
Hb
102
Extinction Coeff (1/cm M)
WAVELENGTH (NM)
HbO
2
400 500 600 700 800 900 1000
as metabolic activity
Deoxyhemoglobin has lower
absorption than oxyhemoglobin in the blue and green
  Bright red arterial blood
  Bluish venous blood
Absorption peaks for HbO2
  418, 542, 577, and 925 nm
Absorption peaks for Hb
550, 758, 910 nm
Isosbestic points
  547, 569, 586, and 798 nm

## Slide 16: Absorption
3.0
0.05
0.06
Water
Lipid (Fat)
Important energy store in the body
1.5
2.0
2.5
0.03
0.04
HB
0.5
1.0
0.00
0.01
0.02
HEMOGLOBIN (1/mm mM)
HbO
2
Lipid
WATER & FAT (1/ mm mM)
Site-specific measurements of body composition
Monitoring of physiological
600
700 800
900
1000
0.0
changes in female breast tissue
Tissue layer model
WAVELENGTH (nm)

## Slide 17: Scattering
Change of direction of propagation and/or energy of
light by a molecular species
Diagnostic applications: Scattering depends on the size, morphology, and structure of the components in tissues (e.g. lipid membrane, collagen fibers, nuclei).
Variations in these components due to disease would affect scattering properties, thus providing a means for
diagnostic purpose
Therapeutic applications: Scattering signals can be
used to determine optimal light dosimetry and provide useful feedback during therapy

## Slide 18: Scattering
Purely absorbing
With Scattering
Photon pathlength >> L
Photon pathlength = L
L
Lambert- Beer Law does not apply here!!! Need to calculate true pathlength of light

## Slide 19: Scattering
Why is the sky blue, clouds white, and sunsets red?
  Blue skies are produced due to scattering at shorter wavelengths
    Visible light (violet & blue) are selectively scattered by O2 and N2 – much smaller than wavelengths of the light
    violet and blue light has been scattered over and over again
  When light encounters larger particles (cloud, fog), Mie scattering occurs
    Mie scattering is not wavelength dependent – appears white
    Cigarette smoke, too
  At sunset
    The light must travel over a longer path in the atmosphere
    Blue/green is scattered away and only red/orange (scattered less) reaches your eyes

## Slide 20: Scattering
Mechanism for Light Scattering
  Light scattering arises from the presence of heterogeneities within a bulk medium
    Physical inclusions
    Fluctuations in dielectric constant from random thermal motion
  Heterogeneity/fluctuations  non-uniform temporal/spatial distribution of refractive index in the medium
    Passage of an incident EM wave sets electric charges into oscillatory motion and can excite vibrational modes
    Scattered light is re-radiated by acceleration of these charges and/or relaxation of vibrational transition

## Slide 21: Scattering
Elastic scattering: no energy change
  Frequency of the scattered wave = frequency of incident wave
  Probes static structure of material
  Rayleigh and Mie scattering
Inelastic scattering: energy change
  Frequency of the scattered wave ≠ frequency of incident wave
  Internal energy levels of atoms and molecules are excited
  Probes vibrational bonds of the molecule
  Raman scattering (stokes↓ and anti-stokes ↑)

## Slide 22: Scattering
Elastic Scattering
The light scattered by a system
has interacted with the inhomogeneities of the system
Photons are mostly scattered
by the structure whose size matches the wavelength
Principal parameters that affect scattering
  Wavelength, λ
  Relative refractive index
  Particle radius
  Shape and orientation
Two types of scattering: Rayleigh and Mie

## Slide 23: Scattering
Rayleigh Scattering
Light Source
Detector
Scattering from very small particles  ≤ λ/10
Rayleigh scattering is inversely related to fourth power of the wavelength of the incident light
4
I  1
λ is the wavelength of the incident light I is the intensity of the scattered light

## Slide 24: Scattering
Mie Scattering
For scattering of particles comparable or larger than the wavelength, Mie scattering predominates
Because of the relative particle size, Mie scattering is not strongly wavelength dependent
Forward directional scattering

## Slide 25: Scattering
Pin =IoA
Pscatt = Ios
Pout = Io(A-s)
Incident Beam
Outgoing Beam
Scattering Cross Section, σscatt [m2]
  ‘area’ of an index-matched, perfectly absorbing disc necessary to produce
The measured reduction of light
σscatt = Qs*As
  Qs: Scattering efficiency (calculated by Mie theory); defined as the ratio of the scattering section to the projected area of the particle on the detector
  As: Area of Scatterer [m2]

## Slide 26: Scattering
Scattering Coefficient, μs [1/m]
  μs =Nsσs ,
    Ns = the number density of scatterers
    σs = scattering efficiency
  Cross-sectional area for scattering per unit volume of medium
Scattering Mean Free Path, ls
  Average distance a photon travels between scattering events
s
s

l  1

## Slide 27: Scattering
d
Scatterer
photon
hv
scattered S’
Anisotropy, g
  Imagine that a photon is scattered by a particle so that its trajectory is deflected by an angle, θ
S
Incidenet Photon
Scattering Angle ()
cos ()
hv
Photon trajectory
Then, component of a new trajectory aligned forward direction is cos(θ)
Anisotropy is a measure of forward direction retained after a single scattering event, < cos(θ)>
Scattering event
 1totally backward scattering

g   0
Biological Tissues: 0.65 < g <0.95

 1
isotropic scattering
totally forward scattering

## Slide 28: Scattering
Reduced Scattering Coefficient, μs’ [1/m]
  μs’ incorporates the
scattering coefficient, μs
and the anisotropy factor, g
s '  (1  g)s
μs’ can be regarded as an
effective isotropic scattering coefficient that represent the cumulative
 26o
effect of several forward- scattering events
Special significant with
respect to photon diffusion theory
g  cos  0.90
s '  (1 g)s  0.10s
mpf  1/ s
mpf '  1/ s '  10mpf  10 / s

## Slide 29: Scattering
Scattering in Tissue
  Tissue is composed of a ‘mixture’ of Rayleigh and Mie scattering
cells
10 m
nuclei
mitochondria
1 m
lysosomes, vesicles
Mie Scattering
striations in collagen fibrils macromolecular aggreagates
0.1 m
Rayleigh Scattering
membranes
0.01 m

## Slide 30: Scattering
Scattering in Tissue
  Refractive index mismatch
between lipid and
surrounding aqueous medium
    Soft tissues are dominated by lipid contents
    Celluar membranes, membrane
folds, and membraneous structure
  Mitochondria, ~ 1m
    Intracelluar organelle
composed of many folded membrane, cristae
  Collegan fibers, 2 ~ 3m
    Collegan fibrils, 0.3 m
    Periodic fluctuation in collegan
ultrastructure source of
Rayleigh scattering in UV and Visible range
  Cells

## Slide 31: Light Transport in Tissue
Modeling of light transport in tissues are often governed by the relative magnitudes of optical absorption and scattering
μa >> μs’ : Lambert-Beer Law (λ ≤300nm;λ≥2000nm)
μs’ >> μa : Diffusion Approximation (600nm ~ 1000nm)
μs’ ~ μa : Equation of Radiative Transfer, Monte Carlo (300nm
~ 600 nm; 1000nm ~ 2000nm)
Use Monte Carlo, Transport Theory, or Diffusion Theory
Physical Pathlength: Lp
Optical Pathlength: Lo
Biological Tissue Lo/Lp = 4 or ↑

## Slide 32: Light Transport in Tissue
Modeling Photon Propagation
a, s, g, phase function S “Stochastic” Description